## Slide 1
Real-time Software Engineering
(RTSE)
Week 2
Department of software engineering
Faculty of Computing
UTM

## Slide 2
Introduction
SCSJ 4423 – Real-time Software Engineering
Challenges in ERT systems
Software development lifecycle
Software engineering essential for ERT
Conclusion

## Slide 3
Introduction
SCSJ 4423 – Real-time Software Engineering
Survey (2005) on embedded systems design completions –
in all applications, > 51% are behind schedule!

## Slide 4
Introduction
SCSJ 4423 – Real-time Software Engineering
Product
Development
Challenges
Software
Engineer

## Slide 5
Product challenges
SCSJ 4423 – Real-time Software Engineering
Product
Memory
Processing
power
I/O
Resource
constraint
Many ERTS have complex life-cycle & require multi-disciplinary skills

## Slide 6
Software engineer challenges
SCSJ 4423 – Real-time Software Engineering
Software
Engineer
Complex team
members
Large team
members
team of s/w engineers is required
to complete the work in time
not many s/w engineers have the
multi-disciplinary skill required in ERTS

## Slide 7
Software development challenges
SCSJ 4423 – Real-time Software Engineering
Development
“One size fits all” technology no longer works

## Slide 8
Software Development for ERT
SCSJ 4423 – Real-time Software Engineering

## Slide 9
Software Development for ERT
SCSJ 4423 – Real-time Software Engineering

## Slide 10
Software Development for ERT
SCSJ 4423 – Real-time Software Engineering
Requirements
Architecture &
Design
Implementation
Verification &
Validation
Clear software development
Framework will ensure the
Successful of ERT system

## Slide 11
Software Development for ERT…example for requirements specification
SCSJ 4423 – Real-time Software Engineering
Autonomous Mobile Robot Requirement
The AMR consists of a body and a pair of wheels. Each drive wheel is move by a direct-current (DC) motor. The speeds of the motors are sensed using shaft encoders and fed back to the embedded controller for computation of control signal to the DC motor every 100 milliseconds using the proportional-integral (PI) control algorithm. The embedded controller also monitors the robot environment using four infrared (IR) proximity sensors and communicates with human using Liquid Crystal Display (LCD) and switches.
Issues that must be addressed in the requirement specification phase for ERT system are :
  functional modeling,
  behavior modeling,
  timing,
  man-machine interface and
  hardware-software interface.
Requirements

## Slide 12
Software Development for ERT
SCSJ 4423 – Real-time Software Engineering
Architecture &
Design
Modeling
Object Oriented
Technology
Scheduling

## Slide 13
Software Development for ERT
SCSJ 4423 – Real-time Software Engineering
Implementation
ERT can be implemented on a single or multi processor and multi tasks are designed to run on one single processor.
To implement multitasking or concurrency in ERTS, 2 software engineering principles need to be considered (Burn and Welling, 1996) are:
  real-time design methodology, which leads naturally into multitasking or concurrency implementation.
  how to undertake or support multitasking and concurrency in the implementation stage. There are 2 ways to support the factor either
    using concurrent real-time language (e.g. ADA) or
    use a sequential language together with a RTOS.

## Slide 14
Software Development for ERT
SCSJ 4423 – Real-time Software Engineering
Verification &
Validation
Programmer
simulator
Main advantages of the proposed simulation strategy are:
  Testing can be done concurrently with the dev. of robot H/W.
  Communication through the H/W interface provides isolation between dev. of simulation.
  Code for H/W interface is similar and provide realistic timing to the actual robot H/W interface.

## Slide 15
Interest of software engineer in ERT system
SCSJ 4423 – Real-time Software Engineering
Well-trained
programmer
Rich knowledge
In programming
Related language
Well-trained
In software development
process
Adaptable

## Slide 16
Task of software engineer in ERT system development
SCSJ 4423 – Real-time Software Engineering
To ensure the success of SE in addressing ERT systems problem, Stankovic, 1996, suggested SE will need to undergo a radical shift :
  Time, dependability, and other QoS constraints must become first-class concerns, coherently integrated with functionality at all levels from requirements specification through architecture, design, implementation, and execution.
  Evolvability must be ensured by separating platform-dependent concerns from application concerns .
  Software must be structured into compose-able modules in which interfaces capture not only functionality.
  Timing constraints, in particular on individual components, must be dynamically derived and imposed on the basis of end-to-end requirements.

## Slide 17
SCSJ 4423 – Real-time Software Engineering
Thank You

## Slide 18
Problem solving
SCSJ 4423 – Real-time Software Engineering
Start with your group
Refer e-Learning